## Slide 1
Drone Search and Rescue:
Finding People and Handing Over Supplies
Team: Barak Loebenstein, Asaf Havia
Academic Advisor: Dr. Jessica Cauchard
Project Number: 2020-01-066

## Slide 2
Search and Rescue

## Slide 3
DRONES
USES IN THE MARKET
The field is evolving rapidly
Improvements in hardware and software
Various Industry and Personal uses

## Slide 4
Speed
#
Mobility
#
Affordability
#
Scalability
#
DRONES
ADVANTAGES

## Slide 5
“A new study on the effectiveness of drones in finding lost individuals demonstrates drones can be an excellent tool”
Conducted by DJI, the European Emergency Number Association, and Black Channel

## Slide 6
Create a Human-Drone Interaction
Our Project’s Goal:

## Slide 7
Handover Interaction Device
Changeable Device
Easy To Program
Modular
Short Learning Time

## Slide 8
Work Plan
Parameters
Flying Speed
Release Height
Distance from the person
Deliver a Device
Tethered
Landing
Drone’s Flight
Scanning
Face Detection
Tracking
Communication Interface
Design an Interface
Language options

## Slide 9
OpenCV package
Face Detection
Front Tracking
Tracking
Waiting for steadiness
Identification
Algorithm
Waiting for consistent faces
Scanning
* DJI Tello , Python 3, Windows

## Slide 10
Face Detection - opencv
* Haar Cascade

## Slide 11
Tracking

## Slide 12
Tracking
Jitter
Offset Box

## Slide 13
Tracking
0
1
2
3
4
5
Face size: 2
X
Y
Z
Target Vector – X , Y , Z
Calculate Differences
Jitter
Offset Box

## Slide 14
Tracking
0
1
2
3
4
5
Face size: 2
Movement – ( 0 , -S , -S)
Correcting
Target Vector – X , Y , Z
Calculate Differences
Jitter
Offset Box

## Slide 15
Tracking
0
1
2
3
4
5
Face size: 3
Movement – ( 0 , -S , -S)
Correcting
Detection rate over a number of consecutive frames
StableObject
Target Vector – X , Y , Z
Calculate Differences
Jitter
Offset Box

## Slide 16
Tracking
Movement – ( 0 , -S , -S)
Correcting
Simulated by landing on the palm
Handover Device
Detection rate over a number of consecutive frames
StableObject
Target Vector – X , Y , Z
Calculate Differences
Jitter
Offset Box

## Slide 17
Parameters Tuning
Number of consecutive frames
Scanning
Notes: In this part I'm going to explain how we got the parameters we defined earlier
In the scanning part we found out that sometime the drone false detect a face what cuese him to stop at the wrong place
We demand consecutive number of positive identifications, we execute a test as shown in the slide where we ran the scanning part when there is no person in the area and checked if the drone can complete a full round

## Slide 18
Parameters Tuning
Chart: Detection by Number of Consecutive Frames
| 1 | 2 | 3 | 4 | 5
Success | 0 | 0.1 | 0.9 | 1 | 1
Number of consecutive frames
Scanning
Notes: We performed 10 tries for each number of consecutive frames. When the numbers of frames were too low, the drone would falsely detect faces and stop to scan in the wrong place. 4 consecutive frames had shown the best result for the minimum requirement and we chose to use this parameter.

## Slide 19
Parameters Tuning
Number of consecutive frames
Scanning
Number of consecutive frames
Tracking Distance
Notes: We wanted to check the best distance for best tracking, when the drone is too close to a person it tends to lose track of the person, when the drone is too far from a person it tends to get many noises and false detections.
We did the same routine in the same speed as shown for moving in front of the drone and counted the number of times the drone lose track
we define success when the drone successfully completes a full trajectory and succeed in following the subject to the starting point.

## Slide 20
Parameters Tuning
Number of consecutive frames
Scanning
Number of consecutive frames
Tracking Distance
Chart: Percent of Full Tracking
| 1 | 2 | 3 | 4 | 5
סידרה 1 | 0.2 | 0.5 | 0.85 | 0.75 | 0.75
Notes: We ran 20 tries for each distance between 1-5.
Distance number 3 gave as the best tracking result and therefore was the selected distance in our program

## Slide 21
Parameters Tuning
Number of consecutive frames
Scanning
Number of consecutive frames
Tracking Distance
Counter = 45 , Reset = 15 , cons_frames = 10
Detection Rate
Notes: we wanted to check the detection rate
at first, when we ran the identification part without demanding a ratio of positive detection, we found out that the drone couldn't identify that the person is not moving.
we did the same routine as before only now we ask for the person to stay still after completing the trajectory.
we checked how long would it take to the drone to reach a steady state.
we ran the test in two conditions; optimal condition in terms of lighting and non optimal with deems lights and wearing glasses

## Slide 22
Parameters Tuning
Number of consecutive frames
Scanning
Number of consecutive frames
Tracking Distance
Counter = 45 , Reset = 15 , cons_frames = 10
Detection Rate
Chart: Average Counter Resets
| 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Resets | 1.4 | 1.7 | 1.6 | 2.2 | 2.4 | 2.555
Chart: Time To Deliver
| 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Resets | 19.2 | 19.9 | 21.2 | 20.8 | 22.1 | 23.5
Optimal Conditions
Chart: Average Counter Resets
| 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Resets | 3.2 | 7.7 | 14 | 18.1 | 20 | 20
Chart: Time To Deliver
| 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Resets | 22.4 | 26.5 | 38.6 | 58 | 60 | 60
Non-Optimal Conditions
Notes: we found out that in a optimal condition the ratio of positive frames is not that important. when there is non optimal condition the ratio had a lot of influence
when we tried for less then 50 % the drone false identify the person is not moving
finally, we chose 50% in our program

## Slide 23
DEMO VIDEO
Notes: Finally, we created a fully working, proof-of-concept with a small sized drone that can be extended to bigger drones in the future.

## Slide 24
Limitations
You can simply impress your audience and add a unique zing and appeal to your Presentations. Easy to change colors, photos and Text.
Performing User Studies
You can simply impress your audience and add a unique zing and appeal to your Presentations. Easy to change colors, photos and Text.
Ordering Technical Parts

## Slide 25
Summary
SAR help
Can be extended for various uses
Information Gain
Add information for a better planning of the mission
Human Drone Interaction
Develop an effective interaction
Drone Capabilities
Use the drone’s advantages in order to get better results

## Slide 26
THANK YOU
FOR LISTENING